# RADIO FUNDAMENTALS

By Maj Rob Robinette

# Electromagnetic Spectrum

Radio waves are made up of electromagnetic energy (similar to light)

Electric lines of force and magnetic lines of force, 90 degree angles to each other

Electric lines of force define horizontal or vertical polarization

Radio waves travel at the speed of light

186,000 miles per second

300 million meters per second

Hertz – cycles per second

Kilohertz (kHz) thousands of cycles per second

Megahertz (MHz) millions of cycles per second

Gigahertz (GHz) billions of cycles per second

Wavelength – distance from peak to peak (example: 17 meter shortwave)

Sound 1 – 20,000 Hertz

Very Low Frequency (VLF) – Submarine communication

Low Frequency (LF) – NDB

Medium Frequency (MF) – AM radio broadcast (1210 kHz, 1.21 MHz)

High Frequency (HF, short wave) – 3 MHz to 30 MHz

Very High Frequency (VHF) – 30 MHz to 300 MHz (FM broadcast 93.7 MHz)

Ultra High Frequency (UHF) – 300 MHz to 3 GHz (cell phone 870 MHz, GPS 1.5 GHz)

Super High Frequency (SHF, a.k.a. microwaves) - > 3 GHz (satellite 4.4 GHz and up)

### ADF Radio

Low and Medium Frequency AM and CW (continuous wave or carrier)

190 to 1750 kHz (1.75 MHz) – Beacons normally 190 – 535kHz CW

Can tune in AM broadcast stations

### VHF Radio AM 108 – 138 MHz

Navigation 108 – 118MHz, voice 118 – 136 MHz

DME 962 – 1213 MHz ; glide slope 329.15 – 335 MHz ; outer, middle, inner markers 75 MHz

Two antennas #1 on bottom, #2 on top (usually better for ground ops)

Line of sight, Guard 121.5 MHz

### UHF Radios AM 225 – 400 MHz

Amplitude Modulation (AM)

Line of sight

Bounces off objects better than VHF

Two antennas #1 on bottom, #2 on top (usually better for ground ops)

Guard 243 MHz (VHF guard times 2)

The C-141 “stinger” HF antenna is horizontally polarized; the VHF and UHF antennas are vertically polarized

### HF Radios SSB, AM  2 MHz - 30 MHz

Range 0 – 13,000 miles (anywhere on Earth)

Antenna and coupler (tuners) in T-tail

Coupler is pressurized to 7 psi +-1 to prevent arcing

Has dual tuners, dual receive but can transmit on one at a time

Max tune time 10 seconds (change freq and try again or try another freq)

Five minutes transmit, five minutes off

Single Side Band (SSB, upper side lobe)

Can transmit AM but no reason to

Use AM to listen to broadcast shortwave stations (BBC, VOA)

Most noise is caused by lightning

Ground wave (0-90 miles, lower freq = more distance)

Dead zone between ground wave and reflected wave

Sometimes weak scatter signals can be heard

Propagation (bending of radio waves, a.k.a. skip)

Skywave radio wave bounces off E and F layers

Can have multiple bounces

Ionosphere – free electrons & ions

D Layer – absorbs radio waves

E Layer – 70 miles high, highest ionization at noon, unreliable (sporadic)

F1 Layer – 100 miles high, some reflection

F2 Layer – 200 miles up, main cause of reflection, 2-13 MHz

### HF radio waves reflecting off the ionosphere

# Refraction and reflection of HF radio waves

Check WWV time signals for propagation

2500  5000  10,000  15,000 and 20,000 kHz (AM)

Long Path – the long way around the earth

Maximum Usable Frequency (MUF)

Freqs close to MUF are best (higher don’t bounce, lower get absorbed by ion layer)

Goes up and down with sun

Sunspots

More sunspots = more ionization and better HF propagation

Can have too much of a good thing

Solar flare can stop HF com and damage satellites

Runs in 11 year cycles, Summer 2000 will be max, 2006 will be minimum