# Text boxes

Diagram not to scale

User assumes responsibility for accuracy and currency

8

7

6

TURN TO FINAL:  App+10; Pwr 1.21 EPR/3600lbs/FF; 0( pitch; Flaps Landing if high and/or hot

FINAL:  600; AGL at 2 SM; Approach A/S (A+0); -2.5(; On Glideslope; Pwr 1.19 EPR/3400lbs/FF

TURN OUT:  Vmfr; 400’ AGL; Field boundary

NO FLAP:  Extend base turn to 3 + SM; Base leg no closer than 3.5 SM from RWY; inform tower of longer final

FOR TRAINING ONLY

5

VFR ENTRY:  Flaps & Gear up; 200 kts; +2( pitch; Pwr 1.1 EPR/2500lbs/FF; 1000’ standard pattern alt (but can be up to 1500’ or as assigned by tower

DOWNWIND:  Check displacement; At mid field - FLAPS APP; GEAR DOWN; App+30; -2( pitch; Pwr 1.25 EPR/4000lbs/FF; (As flaps are passing 40(, lower nose 4(, 4 secs of down trim, 4000lbs FF)

TURN TO BASE:  Before landing check complete; turn at 2 SM/45(/ or past abeam T & G aircraft on final

BASE:  App+20; -1(; Pwr 1.23 EPR/3800lbs/FF; 800’ AGL; clear for straight-in traffic

3

4

2

1

VFR Patterns