# Text boxes

NOTE:  Add 1000 PPH for three engine fuel flow settings

6

5

4

6

3

2

1

| ALL BASED ON 200,000 LB GROSS WEIGHT |
| --- |
| ATT | CONFIGURATION | ASPD | FF | EPR | PITCH |
| LVL | CLEAN | 200 | 2500 | 1.10 | +2 |
| LVL | CLEAN | 250 | 3000 | 1.15 | +1 |
| LVL | CLEAN | 260 | 3500 | 1.20 | +0 |
| LVL | FLAPS APP/GEAR DN | A+30 | 4000 | 1.25 | -2 |
| LVL | FLAPS APP/GEAR DN | A+20 | 3800 | 1.23 | -1 |
| LVL | FLAPS APP/GEAR DN | A+10 | 3600 | 1.21 | 0 |
| LVL | FLAPS LNDG/GEAR DN | APP | 5000 | 1.35 | +1 |
| 2.5( DES | FLAPS LNDG/GEAR DN | APP | 3400 | 1.19 | -2 |
| 2.5( DES | FLAPS APP/GEAR DN | APP | 2800 | 1.13 | -2.5 |
| 1000FPM | FLAPS LNDG/GEAR DN | APP | 2500 | 1.10 | -5 |
| LVL | NO FLAP/GEAR DN | A+30 | 3000 | 1.15 | +3 |
| 2.5( DES | NO FLAP/GEAR DN/+10 HDWD | APP | 2000 | 1.05 | +3 |
| 2.5( DES | NO FLAP/GEAR DN/0 HDWD | APP | 1500 | 1.02 | +3 |
| 2.5( DES | NO FLAP/GEAR DN/-10 TLWD | APP | 1000 | 1.00 | +3 |

Precision Approach:

From FAF to DH: Pwr 1.19 	EPR/3400 PPH; 	Flaps Landing

Non-Precision Approach:

From FAF to MDA: Pwr 1.1 EPR/2500 PPH; 	Flaps Landing

After level-off at MDA: Pwr 1.35 EPR/ 	5000 PPH; Flaps Landing

DOG LEG TO FINAL:  Same as base

FINAL (Before FAF): App+10; Pwr 1.21 EPR/3600 lbs/FF; Flaps Approach

FINAL (After FAF): App+0; Flaps Landing

DESCENT AND ARRIVAL:  Flaps & Gear up; 250 SLOWING TO 200 kts; +2( pitch; Pwr 1.1 EPR/2500 PPH; Altitude as assigned by ATC

DOWNWIND:  FLAPS & GEAR UP; 200 Kts; +2( pitch; Pwr 1.1 EPR/2500 PPH; Approach Check Complete

BASE: FLAPS APP; Gear Down; App+20; -1(; Pwr 1.23 EPR/3800 PPH; Before Landing Check complete

Diagram not to scale

User assumes responsibility for accuracy and currency

FOR TRAINING ONLY

Typical Radar Pattern